## Slide 1: GWC Spring Session 3!
March 8th, 2021
Notes: Names: Hannah, Megan, Zuha, Ana + Paula, Angel, Sasha, Nina

## Slide 2: Today’s Agenda
Accounts and Software
Women-in-Tech Spotlight
Kahoot
Finish Potentiometer and LED circuit!
Servo motor review and lesson 
Stand ups

## Slide 3: Women in Tech Spotlight

## Slide 4: Kahoot!

## Slide 5: Finish Pot-LED cxt

## Slide 6
Command bank
pinMode() - Use the pinMode() command to declare these pins as OUTPUT
analogWrite(pin, value) - to set the brightness of the LEDs, use the analogWrite(pin, value) command.
readValue = analogRead(A0) - Use readValue to store the value of the potentiometer
writeValue = readValue / 4; // divide the readValue by 4 and store as the writeValue
Pseudo code
1) Create variables to store input and output information. 2) Setup the Arduino pins as output pins. 3) Start the main loop.
  a) Store the value of the potentiometer as a variable. b) Determine the output value to the LEDs based on the potentiometer variable. c) Set the LED brightness based on the output variable.
4) End the main loop.

## Slide 7
1. Code Skeleton –> place these in the right order!!!
2. Use this code to fill in the skeleton!
Pseudo code (to help you determine the right order)
1) Create variables to store input and output information. 2) Setup the Arduino pins as output pins. 3) Start the main loop.
  a) Store the value of the potentiometer as a variable. b) Determine the output value to the LEDs based on the potentiometer variable. c) Set the LED brightness based on the output variable.
4) End the main loop.
(A0);
( 9,
( 9,

## Slide 8
https://studentkit-registration.arduino.cc/login

## Slide 9
https://studentkit-registration.arduino.cc/login

## Slide 10: Servo Motor Review and Lesson

## Slide 15: Stand Ups!

## Slide 16: Resources Review:
Student kit (all the circuit diagrams and code we used in the club): https://studentkit.arduino.cc/
Arduino tutorials: https://www.arduino.cc/en/Tutorial/HomePage?from=Main.Tutorials
MIT’s Scratch program is a great stepping stone that uses block coding, allowing you to learn the structure of programming before learning the actual languages themselves.
Code.org provides numerous resources connected to coding for those interested in learning the basics.
Code Academy is an interactive guide to learning multiple languages like JavaScript, HTML/CSS, and more.
Khan Academy has instructional courses on computer programming and computer science, it is an especially good resource for learning how to animate with code.
Also if you have any computer science classes offered at your school, I highly recommend taking them.
Typershark or any basic typing tutorial/software/class. Might seem boring, but proper typing skills will pay off in the future a thousand times over – you don’t want something so simple holding you back!
Maybe robotics and programming isn’t as interesting as you thought it would be, or maybe it’s just not enough! Explore these adjacent fields: Data Science, Robotics, Graphic Design, Engineering, Cybersecurity, Hacking, Machine Learning, Natural Language Processing, Network Design, Website creation.

## Slide 17: Potentiometer
How it works: Inside the potentiometer is a resistive material and a wiper that slides along the material. Each end of the material is connected to a pin. The third pin is connected to the wiper and the resistance depends on the position of the wiper. The potentiometer changes the resistance in the circuit by having more resistive material for the current to pass through, increasing the resistance.
Potentiometer symbol in a circuit:

## Slide 18
int readValue = 0;
int writeValue = 0;
void setup() {
pinMode(9, OUTPUT); // declare the first LED pin as output
pinMode(10, OUTPUT); // declare the second LED pin as output
pinMode(11, OUTPUT); // declare the third LED pin as output
}
void loop() {
readValue = analogRead(A0); // store the value from the potentiometer
writeValue = readValue / 4; // divide the readValue by 4 and store as the writeValue
analogWrite(9, writeValue); // set LED 1 brightness to writeValue
analogWrite(10, writeValue); // set LED 2 brightness to writeValue
analogWrite(11, writeValue); // set LED 3 brightness to writeValue
}

## Slide 19: Code Review:
COLORS[] is an _________
GREEN is a ______
The ______of YELLOW in COLORS[] is two
green_light() is a ____________
Word bank:
array
variable
function
index

## Slide 20: Women in Tech Spotlight: Tan Le
Accomplishments
Tan Le is the CEO and founder of Emotiv - a bioinformatics company.
The company is exploring a new “remote control” where a headset uses EEG technology to control digital devices by reading brain activity.
She is a refugee from Vietnam at age 4, she entered college at 16 and has since become a vital young leader in her home country of Australia. She attended Monash University in Melbourne, Australia where she studied law and commerce.
https://www.ted.com/talks/tan_le_a_headset_that_reads_your_brainwaves

## Slide 21: Review: Servo Motor

## Slide 22: Circuit Review: Series vs Parallel
????
????
Electricity has two parallel paths!
Electricity has one path and must go through both components one after another, i.e. in series!

## Slide 23
Light Wave RADAR